## Slide 1: Talk outlines
Introduce partial synthesis and its QBF formulation
Computing inductive invariants with partial synthesis
Discussion on IC3/PDR-like analysis with inductive invariants
Use of inductive invariants for control FSM analysis, logic optimization, ATPG for stuck-at faults avoiding over testing
Use of partial synthesis for Engineering Change Order (ECO)
  Complete verification with small numbers of test vectors by utilizing “templates”

## Slide 2: Toward Unification of Synthesis, Verification and Testing in Topologically Constrained Logic Design
Masahiro Fujita
VLSI Design and Education Center
University of Tokyo
Extended version of
Masahiro Fujita: Toward Unification of Synthesis and Verification in Topologically Constrained Logic Design. Proceedings of the IEEE 103(11) 2052-2060(2015)

## Slide 3: Key observation for the talk
Design is a “black box” combinational circuit
  In order to determine the logic function realized by the design, we need to check 2n of test vectors where n is #number
Design must follow some constraints, such as keeping the circuit topology
  Do we still need 2n of test vectors ???
  Only experimentally shown
Circuit2
n
n
Topologically Constrained Logic Design
Notes: この手法では組み合わせ回路を対象とする。

## Slide 4: Entire circuit is black box
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x
y
f
Truth table for entire circuit
x | y | f
0 | 0 | P1
0 | 1 | P2
1 | 0 | P3
1 | 1 | P4
Entire set of implementable logic functions

## Slide 5: Only sub-circuit is black box (1)
x
y
Truth table for entire circuit
x | y | g
0 | 0 | Q1
0 | 1 | Q2
1 | 0 | Q3
1 | 1 | Q4
Entire set of implementable logic functions at f (16 functions)
g
f
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 6: Only sub-circuit is black box (2)
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x
y
Truth table for entire circuit
x | y | g
0 | 0 | Q1
0 | 1 | Q2
1 | 0 | Q3
1 | 1 | Q4
Entire set of implementable logic functions at g (only 4 functions)
g
g1
g1
g1
g1
g2
g2
g2
g2
g3
g3
g3
g3
g4
g4
g4
g4
f

## Slide 7: Complete sets of test patterns
Entire circuit is black box
  Need 22 test patterns to determine the function
Only sub-circuit is black box
  Need only 2 test patterns, (0,1) and (1,1) to determine the function
x
y
f
Truth table for entire circuit
All 16 functions possible
(P1,P2,P3,P4)=(0,0,0,0),(0,0,0,1),
…,(1,1,1,1)
x | y | f
0 | 0 | P1
0 | 1 | P2
1 | 0 | P3
1 | 1 | P4
x
y
x | y | g
0 | 0 | Q1
0 | 1 | Q2
1 | 0 | Q3
1 | 1 | Q4
g
f
Truth table for entire circuit
Only 4 functions possible
(Q1,Q2,Q3,Q4)=(0,0,0,0),
(0,0,0,1),(0,1,0,0),(0,1,0,1)
Note: These are complete sets of test vectors!

## Slide 8: The basic problem: Partial logic synthesis
A set of subcircuits are vacant
Inputs to the subcircuits have been fixed (no change)
Vacant subcircuits should be filled in such a way that entire circuit becomes correct
We do not know those functions, but we know the inputs
  Use Look Up Table (LUT) for each of subcircuit
Vacant subcircuit1
C1
Entire circuit
Vacant subcircuitn
Cn
Vacnt subcircuit2
C2
…
X
Not allowed
These can be any logic functions

## Slide 9: LUT (Look up Table) is nothing but MUX
Any logic function with m-inputs
  MUX with m-control inputs
  2m variables for truth table values
…
…
i0
i1
im
p0
p1
p
p
2m-2
2m-1
out
MUX
2m-1
p0, p1, …, p represent values of truth tables (ProgVars)
By changing those values, any logic function with m-input can be represented
  If i0 then out = p0 AND
  If i1 then out = p1 AND
  …
  If i then out = p
Only one of p0, p1, …, p is connected to out
2m-1
2m-1
2m-1

## Slide 10: Problem formulation
Look up Table (LUT) can represent all logic functions with the set of inputs
  Introducing programmable variables
Then the problem becomes QBF (Quantified Boolean Formula)
  Given appropriate programming of LUT, the circuit is equivalent to the spec
∃ProgVar.∀Input. f (ProgVar, Input) = TargetNewSPEC(Input)
Input
TargetSPEC(Input)
ProgVar
ProgVar
ProgVar
LUT
LUT
LUT
Remark: This is not a SAT problem!

## Slide 11: A buggy design for a 1-bit full adder
◆Specification
◆A buggy implementation
Erroneous portion
We can solve the problem only with SAT solvers instead of QBF solvers
Sampling based synthesis and refinement
Notes: 提案手法ですが、例を用いて説明したいと思います。
図のように1bitの全加算器を考えます。ゲートの1つを2入力LUTに置き換えます。
LUTの論理はあるLUTの論理Xがあった時、全ての入力ABCに対して2つの回路が等価であるかどうかという
2QBF問題を解くことによって得ることができます。

## Slide 12: A trace of correction for a 1-bit full adder
◆Specification
◆Replace an EOR with LUT
A | B | D
0 | 0 | X1
0 | 1 | X2
1 | 0 | X3
1 | 1 | X4
Truth table for LUT
2-input
LUT
Erroneous portion
Notes: 提案手法ですが、例を用いて説明したいと思います。
図のように1bitの全加算器を考えます。ゲートの1つを2入力LUTに置き換えます。
LUTの論理はあるLUTの論理Xがあった時、全ての入力ABCに対して2つの回路が等価であるかどうかという
2QBF問題を解くことによって得ることができます。

## Slide 13: Simple example: Step1
  Outputs must be equal when inputs are (0,0,0) and (1,1,1)
  These are necessary conditions
0
0
0
0
0
0
1
1
1
1
1
1
EQ check
EQ check
Can be solved as simple SAT problem
If unsat, there is no way to rectify
A | B | D
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Truth table for LUT
LUT
LUT
Current solution
Synthesis from sample values (necessary conditions)
Notes: まず、全ての入力パターンについて検討することは難しいので、一部の入力パターン、ここでは（0,0,,0）(1,1,1)についてのみ考えます。
2つのパタンに対して仕様と等価になるLUTの論理Xを探します。これは、上の式のようなSAT問題に定式化できるので、
回路をCNF形式と呼ばれるSAT問題の表記形式に変換し、解きます。
するとXが００００の時、仕様と等価になるとわかります。
SAT問題を満たす入力が存在しないことをUNSATといいます。
もし、UNSATになる時、２つの回路が等価になるLUTの論理は存在しないことになります。

## Slide 14: Simple example: Step2
  Based on current solution, check if it is actually a real solution
  Outputs can never become non-equal
Typical SAT formulation
If unsat, current solution candidate is real solution
(A,B,C) = (0,1,0)
is a counter example
Non-EQ check
LUT
Notes: 次に先ほど求めたLUTの論理Xが本当に正しいか調べます。
X=００００を代入した時、２つの回路が非等価になる入力ABCが存在するかどうか調べます。
式では、上のSAT問題のように書くことができます。
左図のような回路を記述し、CNF形式に変換し、SAT問題として解きます。
UNSATとなる時、（0000）が求めるLUTの論理となります。
今回は、（0,1,0）の時、出力が異なることがわかります
非等価になる時の入力ABCを反例とイイます。

## Slide 15: Simple example: Step3
  Outputs must be equal when inputs are (0,0,0), (1,1,1) and (0,1,0)
Can be solved as simple SAT problem
If unsat, there is no way to rectify
A | B | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Truth table for LUT
Current solution
0
0
0
0
0
0
1
1
1
1
1
1
EQ check
EQ check
LUT
LUT
EQ check
0
1
0
0
1
0
Notes: まず、全ての入力パターンについて検討することは難しいので、一部の入力パターン、ここでは（0,0,,0）(1,1,1)についてのみ考えます。
2つのパタンに対して仕様と等価になるLUTの論理Xを探します。これは、上の式のようなSAT問題に定式化できるので、
回路をCNF形式と呼ばれるSAT問題の表記形式に変換し、解きます。
するとXが００００の時、仕様と等価になるとわかります。
SAT問題を満たす入力が存在しないことをUNSATといいます。
もし、UNSATになる時、２つの回路が等価になるLUTの論理は存在しないことになります。

## Slide 16: Simple example: Step4
  Based on current solution, check if it is actually a real solution
  Outputs can never become non-equal
Typical SAT formulation
If unsat, current solution candidate is real solution
(A,B,C) = (1,0,1)
is a counter example
Non-EQ check
LUT
0
1
0
0
Notes: 次に先ほど求めたLUTの論理Xが本当に正しいか調べます。
X=００００を代入した時、２つの回路が非等価になる入力ABCが存在するかどうか調べます。
式では、上のSAT問題のように書くことができます。
左図のような回路を記述し、CNF形式に変換し、SAT問題として解きます。
UNSATとなる時、（0000）が求めるLUTの論理となります。
今回は、（0,1,0）の時、出力が異なることがわかります
非等価になる時の入力ABCを反例とイイます。

## Slide 17: Simple example: Step5
  Outputs must be equal when inputs are (0,0,0), (1,1,1), (0,1,0) and (1,0,1)
Can be solved as simple SAT problem
If unsat, there is no way to rectify
A | B | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth table for LUT
Current solution
0
0
0
0
0
0
1
1
1
1
1
1
EQ check
EQ check
LUT
LUT
EQ check
0
1
0
0
1
0
EQ check
1
0
1
1
0
1
Notes: まず、全ての入力パターンについて検討することは難しいので、一部の入力パターン、ここでは（0,0,,0）(1,1,1)についてのみ考えます。
2つのパタンに対して仕様と等価になるLUTの論理Xを探します。これは、上の式のようなSAT問題に定式化できるので、
回路をCNF形式と呼ばれるSAT問題の表記形式に変換し、解きます。
するとXが００００の時、仕様と等価になるとわかります。
SAT問題を満たす入力が存在しないことをUNSATといいます。
もし、UNSATになる時、２つの回路が等価になるLUTの論理は存在しないことになります。

## Slide 18: Simple example: Step5
  Based on current solution, check if it is actually a real solution
  Outputs can never become non-equal
Typical SAT formulation
If unsat, current solution candidate is real solution
Actually unsat, and so this is the solution
Non-EQ check
LUT
0
1
1
0
A | B | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
If necessary, can check if no more solution or not
Notes: 次に先ほど求めたLUTの論理Xが本当に正しいか調べます。
X=００００を代入した時、２つの回路が非等価になる入力ABCが存在するかどうか調べます。
式では、上のSAT問題のように書くことができます。
左図のような回路を記述し、CNF形式に変換し、SAT問題として解きます。
UNSATとなる時、（0000）が求めるLUTの論理となります。
今回は、（0,1,0）の時、出力が異なることがわかります
非等価になる時の入力ABCを反例とイイます。

## Slide 19: Experimental results on partial synthesis
Larger circuits: Time frame expanded OpenRISC
  17,701 gates in combinational part
  2*17,701, 3*17701, 4*17701
Mostly solved
  Average time solved in sec
Small numbers of iterations (test patterns)
  Tens to hundreds
Time frames expanded | #LUT | #solved (5h) | Ave. time when solved (sec)
2 | 10 | 20/20 | 169.1
 | 20 | 20/20 | 277.5
 | 50 | 20/20 | 639
 | 100 | 20/20 | 1153.25
3 | 10 | 20/20 | 646.65
 | 20 | 20/20 | 1114.05
 | 50 | 20/20 | 2820.35
 | 100 | 20/20 | 5668.8
4 | 10 | 20/20 | 1685.4
 | 20 | 20/20 | 3444.45
 | 50 | 20/20 | 9094.35
 | 100 | 10/20 | 12905.3

## Slide 20: When there is no logical specification is available
𝑖𝑛𝑂𝑢𝑡 = ∅
?
?
𝑖𝑛𝑂𝑢𝑡 =
is the solution
No solution
SAT
UNSAT
UNSAT
SAT
Repeat the following until UNSAT
  Generate two solution candidates which satisfy InOut
  Generate input by which the two are distinguished

## Slide 21: QBF-based inductive invariant generation and its application to logic synthesis and IC3/PDR-like verification (on-going)
Masahiro Fujita
VLSI Design and Education Center
(VDEC)
University of Tokyo
Also discussing template based test pattern generation (generalization of mutation based testing)

## Slide 22: Verification and computation of invariants
Given an invariant property
  AG ~(bad)
How to verify?
  Starting with initial states, S0, compute all reachable states, R
  If R does not intersect bad states, design is correct
  If it does, incorrect
If R’, a superset of R, does not intersect bad states, correct
  This is a sufficient condition
  If R’ intersect bad states, no conclusion
S0
R
Bad
S0
R
Bad
So how can we compute R or (useful) R’ efficiently?

## Slide 23: How to compute reachable states ?
Precise computation
  Explicit/implicit ways
  Very expensive for large systems
Approximate computation
  Superset of reachable states
  Still need some iterations
  Still expensive depending on accuracy
Proposed method
  Analysis only on one time frame
    Some similarity to IC3/PDR
  Superset of reachable states are computed based on “given set of state variables”
S0
R

## Slide 24: Breadth-First Reachability Analysis
Ri – set of states that can be reached in i transitions
  Image computation:
Reach fixed point when Rn = Rn+1
  Guaranteed since finite state
Very expensive if circuits becomes larger
  Practically need to compute their approximation such as superset
R0
00
00
10
01
11
R1
R0
00
01
R2
R1
R0
00
01
10
R3
R2
R1
R0
00
01
10

## Slide 25: Bounded reachability
NSk
CL1
CL2
CLk
PI2
POk
PI1
PIk
PO1
PO2
PS3
PS2
PSk
NS1
NS2
NSk-1
PS1
PI
PO
Latches
NS
PS
CL
Unroll k-Steps
Compute reachable states up to k cycles from the initial states
  Gives subsets of reachable states
  Or gives supersets of reachable states depending on how to compute
Here we set k=1

## Slide 26: Approximate computation of reachable states
Most algorithms iterate computation as much as possible
  Bounded computation with as large as possible, k
Each image computation can be approximate
  Computing supersets of the next states
Trade-offs between accuracy and computation time
  Various methods have been proposed
IC3/PDR compute superset of reachable states which are useful for a given property (invariant)
  We will do something similar but with QBF formulation

## Slide 27: The proposed method for reachable state computation
Based on single time frame analysis
  Inductive invariants are computed without iteration
  If f is true in the current state, f is also true in the next state
Defined with Quantified Boolean Formula (QBF)
  But solved by repeatedly applying SAT solvers
  Or solve as a single incremental SAT problem
Combinational
circuit
State variables
Flipflops
in
out
f
f
ffin
ffout

## Slide 28: Inductive invariants
h
Invariant, g
  g is true for all states
  g is true for the specified set of states, h
Inductive invariants
  If f is true in current states, f is also true in their next states
  If f includes initial states, it gives all reachable states
    Or their superset
Here we compute “inductive” invariants
Combinational
circuit
State vars
Flipflops
in
out
f
f
ffin
ffout
Combinational
circuit
State vars
Flipflops
in
out
g
ffin
ffout
Combinational
circuit
State vars
Flipflops
in
out
ffin
ffout
g

## Slide 29: QBF formulation of inductive invariants
If f is true in current states, f is also true in their next states
  ∃ f. ∀ ps,ns. f(ps) => f(ns)
  Quantifier over function
  ps and ns are related through the combinational circuit
Function, f is represented as LUT (Look up Table)
  Any logic function with m-inputs
  MUX with m-control inputs
  2m variables for truth table values
  Note: Exponentially many variables are required !
Combinational
circuit
State vars
Flipflops
in
out
f
f
ffin
ffout
LUT2:
f
LUT1:
f
Same function
Always 1
x
y
Combinational
circuit
State vars
Flipflops
ffin
ffout
ps
ns
m
m
|ff|
|ff|
|ff|
|ff|

## Slide 30: LUT (Look up Table)
Any logic function with m-inputs
  MUX with m-control inputs
  2m variables for truth table values
…
…
i0
i1
im
p0
p1
p
p
2m-2
2m-1
out
MUX
2m-1
p0, p1, …, p represent values of truth tables
By changing those values, any logic function with m-input can be represented
…
Only one of p0, p1, …, p is connected to out
2m-1
2m-1
If i0 i1…i = 00…0 then out = p0 AND
2m-1
If i0 i1…i = 10…0 then out = p1 AND
2m-1
If i0 i1…i = 11…1 then out = p
2m-1

## Slide 31: QBF formulation of inductive invariants
Quantifier over function become quantifier over variables by utilizing LUT based formulation
  ∃ f. ∀ ps,ns. f(ps) => f(ns)
  ∃ p0, p1, …, p . ∀ ps,ns. LUT(ps) => LUT(ns)
LUT2:
f
LUT1:
f
Same function
Always 1
x
y
Combinational
circuit
State vars
Flipflops
ffin
ffout
ps
ns
2m-1
Note: ps and ns are related through the combinational circuit

## Slide 32: &qbfgen of ABC tool
Circuit generated by “&qbfgen –K 3” for s27
  ∃ pi00,pi01,pi02,pi03,pi04,pi05,pi06,pi07.
  ∀ pi08,pi09,pi10,pi11,pi12,pi13,pi14. LUT(ps) => LUT(ns)
  pi00 must be 1 as it is the initial state
LUT2:
f
LUT1:
f
Same function
Always 1
x
y
Combinational
circuit
ps
ns
~n65
~n64
~n44
po0=~n65&pi00
pi08 pi09 pi10
pi11 pi12 pi13 pi14
n22 n23 n24
po0
Truth table values for LUT

## Slide 33: Discussions
We use LUT to represent the function, f
In practice, up to around 16 inputs for f
  Need exponentially many variables for truth tables
There are so many state variables or flipflops (tens of thousands or much more) in sequential circuits
  QBF solvers do not work for such large problems
  So can work only with subsets of state variables
  Supersets of reachable states are extracted with them
Then the question is, “can we extract inductive invariants with those subsets ?”
  Yes, there are inductive invariants on the subsets in many cases confirmed by experiments
Notes: 先ほど見つけた反例を入力パタンに追加します。
手順１と同様にして、（000）(111)(010)の３パタンについて2つの回路が等価になるLUTの論理を求めます。
この時、SAT問題はこのようになります。
LUTの論理を求める⇨反例を探す⇨反例追加するの流れを繰り返して、LUTの論理を探します。
今回の加算器の例では、入力３パタンで探す⇨LUTの論理が（０１００）となる、反例（１０１）が見つかる。反例追加して入力４パタンでLUTの論理を探す。
(0101)となる。反例が見つからず、これが求めるLUTの論理であるとわかる。という流れになります。

## Slide 34: ISCAS89 s27 benchmark circuit
G5
G0
G1
G2
G3
G6
G7
G14
G13
G8
G15
G9
G1
1
G17
G10
G16
G12
FF
FF
FF
3LUT:
f
3LUT:
f
Same function
Always 1
x
y
There are three flipflops (all zero is the initial state)
With 3-input LUT, complete reachability is obtained
G7G6G5 | 
000 | 1
001 | 1
010 | 1
011 | 0
100 | 1
101 | 1
110 | 1
111 | 0
Inductive invariant/
reachability

## Slide 35: With two state variables (1)
G5
G0
G1
G2
G3
G6
G7
G14
G13
G8
G15
G9
G1
1
G17
G10
G16
G12
FF
FF
FF
2LUT:
f
2LUT:
f
Same function
Always 1
x
y
Invariant computation successful with 2-input LUT
G6G5 | 
00 | 1
01 | 1
10 | 1
11 | 0
G7G6G5 | 
000 | 1
001 | 1
010 | 1
011 | 0
100 | 1
101 | 1
110 | 1
111 | 0
Restrict to G6G5

## Slide 36: With two state variables (2)
G5
G0
G1
G2
G3
G6
G7
G14
G13
G8
G15
G9
G1
1
G17
G10
G16
G12
FF
FF
FF
2LUT:
f
2LUT:
f
Same function
Always 1
x
y
No invariant for these two state variables
G7G5 | 
00 | 1
01 | 1
10 | 1
11 | 1
G7G6G5 | 
000 | 1
001 | 1
010 | 1
011 | 0
100 | 1
101 | 1
110 | 1
111 | 0
Restrict to G7G5

## Slide 37: Another example
abc 01> &r b05.st.aig
abc 01> &genqbf -K 3
abc 01> &qbf -P 8
Parameters: 11111000 Statistics: 0=3 1=5
The problem is SAT after 4 iterations. Time = 0.00 sec
abc 01> read_truth -x 00011111
abc 02> st
abc 03> collapse
abc 04> w tmp.pla
.model b05.blif
.inputs START
.outputs …
.latch U645 STATO_REG_0_ 0
.latch U644 STATO_REG_1_ 0
.latch U643 STATO_REG_2_ 0
.latch U680 NUM_REG_4_ 0
…
b05
i/o=1/36 ff=34 and=830 lev=54
.i 3
.o 1
0-- 1
-00 1
.e
Reversed
Unreachable states are 111, 110, 101 for STATO_REG_0_, STATO_REG_1_, and STATO_REG_2_
.i 3
.o 1
--0 1
00-1
.e
STATO_REG_0_ STATO_REG_1_ STATO_REG_2_
Adjust order

## Slide 38: Now comparison with pdr
&genqbf;&qbf just computes inductive invariants
  No need to be given a property
pdr needs a property
  Property: AG~(unreachable state)
  Output of blif for pdr is out=(unreachable state)

## Slide 39: Running pdr
abc 01> r b05.pdr.blif
abc 04> st
abc 05> pdr -d
Invariant F[6] : 2 clauses with 3 flops (out of 34)
Verification of invariant with 2 clauses was successful. Time= 0.00 sec
Inductive invariant was written into file "inv.pla".
Property proved. Time = 0.02 sec
.model b05.pdr.blif
.inputs START
.outputs out
.latch U645 STATO_REG_0_ 0
.latch U644 STATO_REG_1_ 0
.latch U643 STATO_REG_2_ 0
.latch U680 NUM_REG_4_ 0
…
.names STATO_REG_0_ STATO_REG_1_ STATO_REG_2_ out
011 1 //This is an unreachable state
…
.i 3
.o 1
.ilb STATO_REG_0_ STATO_REG_1_ STATO_REG_2_
-11 1
1-1 1
.e
b05
Complemented
i/o=1/36 ff=34 and=830 lev=54
.i 3
.o 1
--0 1
00- 1
.e
Same as the one generated by &qbf

## Slide 40: Experiments
The proposed method for inductive invariant computation has been implemented as a command on top of logic synthesis and verification tool, ABC (available in regular distribution)
Several experiments on logic synthesis, optimization, and testing have been conducted
Experiments performed (all are using subsets of state variables) :
  Computation of inductive invariants for ISCAS89 circuits
  Control FSM analysis for ITC99 circuits
  Logic optimization with unreachable states for ISCAS89 circuits
  ATPG without using computed unreachable states for ISCAS 89 circuits

## Slide 41: 1. Computation of inductive invariants for ISCAS89 circuits
ISCAS89 s298 circuit has 14 flipflops, 3 inputs and 6 outputs
Inductive invariants are extracted with different numbers of flipflops for the function, f
Number of inputs to LUT | Number of test patterns | Size of on-set in invariant | Time (sec)
2 | 3 | 4 (all1) | 0.04
3 | 7 | 8 (all1) | 0.06
4 | 9 | 10 | 0.07
5 | 19 | 20 | 0.13
6 | 39 | 40 | 0.26
7 | 41 | 43 | 0.33
8 | 51 | 54 | 0.38
9 | 54 | 55 | 0.33
10 | 55 | 56 | 0.38
11 | 55 | 56 | 0.69
12 | 55 | 56 | 0.62
13 | 109 | 110 | 5.67
14 | 217 | 218 | 26.1

## Slide 42: 2. Control FSM analysis for ITC99 circuits
Extract inductive invariants for control FSM
ISCAS89 circuits are first converted into And-Inverter-Graph (AIG)
ITC99 are supplied in:
  Netlists which are processed here
  RTL from which we get possible names of FSM flipflops, such as STAT…

## Slide 43
Circuit | Primry inputs | Flip-flops | Number of inputs to LUT | Number of test patterns | Time (sec) | Extracted invariant
b01 | 2 | 5 | 3 | 6 | 0.06 | 11111111
b02 | 1 | 4 | 3 | 5 | 0.05 | 11111110
b03 | 4 | 30 | 2 | 2 | 0.04 | 1110
b04 | 11 | 66 | 2 | 1 | 0.03 | 1110
b05 | 1 | 34 | 4 | 7 | 0.07 | 1111100001011000
b06 | 2 | 9 | 3 | 5 | 0.05 | 11111110
b07 | 1 | 49 | 3 | 5 | 0.06 | 11111110
b08 | 9 | 21 | 2 | 2 | 0.04 | 1111
b09 | 1 | 28 | 2 | 3 | 0.04 | 1111
b10 | 11 | 17 | 4 | 10 | 0.08 | 1110111011101010
b11 | 7 | 31 | 4 | 8 | 0.07 | 1110101010101010
b13 | 10 | 53 | 2 | 3 | 0.04 | 1111
b15 | 36 | 449 | 8 | 116 | 0.90 | 1000000001111111011111110000000001111111000000000001001100000000011111110111111101111111000000000111111100000000011111110000000000000000011111110111111100000000011111110000000000010011000000000111111101111111011111110000000000111111000000000111111100000000

## Slide 44: 3. Logic optimization with unreachable states for ISCAS89 circuits
Insert a circuit in front which represents external don’t cares
Apply multi-level logic optimizers in normal ways
f
Combinational
circuit
State vars
Flipflops
in
out
ffin
ffout
For flipflops in the invariant
If f is 1, signal values are preserved
If f is 0, zero values are given to combinational circuit
f
Combinational
circuit
State vars
Flipflops
in
out
ffin
ffout
For flipflops in the invariant
If f is 1, signal values are preserved
If f is 0, zero values are given to combinational circuit
0s
0
1

## Slide 45: ISCAS89 circuits after converted into AIG
ISCAS89 circuits are first converted into And-Inverter-Graph (AIG)

## Slide 46: 3. Logic optimization results for ICAS89
Optimized with “mfs2”command in ABC
Around 10-50% reduction with unreachable states as external don’t cares
Many multi-level logic optimizer can be used
Circuit | Before opt | Opt without extDC | Opt with extDC | Ratio with/without
s298 | 282 | 178 | 130 | 0.73
s344 | 416 | 211 | 97 | 0.46
s386 | 425 | 293 | 146 | 0.50
s444 | 397 | 238 | 199 | 0.84
s526 | 490 | 319 | 276 | 0.87
s526n | 490 | 319 | 270 | 0.85
s641 | 594 | 265 | 200 | 0.75
s1196 | 1,050 | 839 | 811 | 0.97
s1238 | 1,082 | 877 | 849 | 0.97
s1488 | 1,483 | 1,205 | 1,021 | 0.85
s1494 | 1,489 | 1,215 | 1,038 | 0.85
s5378 | 4,421 | 2,353 | 2,160 | 0.92
s9234 | 8,241 | 3,553 | 3,185 | 0.90
s15850 | 14,278 | 6,592 | 5,820 | 0.88
s38417 | 33,736 | 18,640 | 16,752 | 0.90
s38584 | 34,250 | 22,592 | 20,485 | 0.91

## Slide 47: 4.1 How much test patterns with regular ATPG uses subsets of unreachable states
Test patterns are generated for single stuck-at faults with combinational ATPG
Check if they intersect computed unreachable states

## Slide 48: ATPG with unreachable states
Add a circuit in front which inhibit the use of (subsets) unreachable states
  Deal only with combinational
With the additional circuit, normal combinational ATPG tools can be used
  Automatically avoid using unreachable states
f
Combinational
circuit
State vars
Flipflops
in
out
ffin
ffout
f
Combinational
circuit
State vars
Flipflops
in
out
ffin
ffout
For flipflops in the invariant
If f is 1, signal values are preserved
If f is 0, zero values are given to combinational circuit
0s
0
1
Optimized
x
x
x
x
x
x

## Slide 49: 4.2 How much test patterns with regular ATPG uses subsets of unreachable states
Test patterns are generated for multiple stuck-at faults with combinational ATPG
Check if they intersect computed unreachable states

## Slide 50: 4.3 Ratio with/without using subsets of unreachable states
Test patterns are generated for multiple stuck-at faults
  Allowing intersection with unreachable states
  Avoid intersecting with unreachable states
ISCAS89 circuits | Test patterns for all multiple faults |  | 
 | Test patterns generated for mutiple faults (no restriction) | Test patterns generated for mutiple faults inside of supersets of reachable states | Ratio (Restriction)/(No restriction)
s1196 | 117 | 398 | 3.40
s1238 | 153 | 548 | 3.58
s13207 | 319 | 923 | 2.89
s1488 | 108 | 284 | 2.63
s1494 | 112 | 357 | 3.19
s15850 | 141 | 793 | 5.62
s298 | 28 | 64 | 2.29
s382 | 27 | 87 | 3.22
s38417 | 182 | 1404 | 7.71
s38584 | 197 | 1595 | 8.10
s386 | 64 | 214 | 3.34
s444 | 26 | 73 | 2.81
s510 | 58 | 110 | 1.90
s526 | 49 | 159 | 3.24
s5378 | 108 | 517 | 4.79
s641 | 25 | 162 | 6.48
s713 | 24 | 148 | 6.17
s9234 | 297 | 794 | 2.67
s953 | 80 | 197 | 2.46
Average | 111.32 | 464.58 | 4.17

## Slide 51: Current problem and future direction
Use LUT to represent function, and so in practice, up to around 16 inputs
  16 inputs need 65,536 variables
  But many state variables or flipflops in real sequential circuits
  Picking up appropriate subsets is not straightforward
Any way to represent functions with many inputs?
  SOP based formulation can accept more inputs as long as the numbers of product terms are not large
    100 inputs and 65 products need 65,000 variables
  Use our method (ATS2016) for selecting inputs for functions without determining the functions
    Any numbers of inputs are OK but the problem must be reformulated (not known how)
Notes: 先ほど見つけた反例を入力パタンに追加します。
手順１と同様にして、（000）(111)(010)の３パタンについて2つの回路が等価になるLUTの論理を求めます。
この時、SAT問題はこのようになります。
LUTの論理を求める⇨反例を探す⇨反例追加するの流れを繰り返して、LUTの論理を探します。
今回の加算器の例では、入力３パタンで探す⇨LUTの論理が（０１００）となる、反例（１０１）が見つかる。反例追加して入力４パタンでLUTの論理を探す。
(0101)となる。反例が見つからず、これが求めるLUTの論理であるとわかる。という流れになります。

## Slide 52: Automatically Adjusting System Level Designs after RTL/Gate-Level ECO
Qinhao Wang, Yusuke Kimura, Masahiro Fujita
University of Tokyo

## Slide 53: C-based design ECO
After generating RTL/gate, ECO (Engineering Change Order) is applied only to implementation designs
(2) RTL
(1) Original system design in C
High level synthesis
Or
Manual design
Logic synthesis
Or
Manual design
(3) Netlist
(4) RTL with ECO
(5) Netlist with ECO
ECO
ECO

## Slide 54: C-based design ECO
After generating RTL/gate, ECO (Engineering Change Order) is applied only to implementation designs
(2) RTL
(1) Original system design in C
High level synthesis
Or
Manual design
Logic synthesis
Or
Manual design
(3) Netlist
(4) RTL with ECO
(5) Netlist with ECO
ECO
ECO
No C descriptions for this

## Slide 55: C-based design ECO
After generating RTL/gate, ECO (Engineering Change Order) is applied only to implementation designs
Try to get a corresponding C from ECOed implementation
  Manual generation may not be easy and could be time consuming
Can we automate this?
(2) RTL
(1) Original system design in C
High level synthesis
Or
Manual design
Logic synthesis
Or
Manual design
(3) Netlist
(6) Restored high level design in C
(4) RTL with ECO
(5) Netlist with ECO
Proposed method: Automatic inferring
ECO
ECO
≠
Due to ECO

## Slide 56: Why it is hard between C/RTL, C/gate?
Even if they are equivalent, their descriptions can be very different (textually or structurally)
  Different ways of implementation styles, scheduling, binding, parallelism, …
Unless information on them are given, very hard to establish mapping of internal signals between the two
  Some tool vendors are doing that way (get them from HLS)
How should we proceed?
  Generate C description from RTL/gate which is similar to the original C
  Even if the two have similar behaviors, is this possible?
    Based on Counter-Example Guided Inductive Synthesis

## Slide 57: Counter-Example Guided Inductive Synthesis
In-out data, InOut, for learning is given (initially empty)
  f(x,y): InOut = { (x=a,y=b), (x=a’,y=b’), ….}
Generate a solution candidate, S, from InOut
  Typically based on user-supplied templates
  The problem can be formulated as Quantified Boolean Formula (QBF) and solved by incremental SAT or QBF solver
  If no solution generated, terminate with no solution
Check if S is correct for all possible inputs by SAT/SMT
  If so, S is actually the solution
  If not, generate a counter example (x=cx, y=cy)
Add (x=cx, y=cy) to InOut, and repeat the above

## Slide 58: When there is no logical specification is available
𝑖𝑛𝑂𝑢𝑡 = ∅
?
?
𝑖𝑛𝑂𝑢𝑡 =
is the solution
No solution
SAT
UNSAT
UNSAT
SAT
Repeat the following until UNSAT
  Generate two solution candidates which satisfy InOut
  Generate input by which the two are distinguished

## Slide 59: Let’s discuss with simple example
Spec: Count numbers of 1’s in an integer word, x
X
N
Count number of 1’s
X = “00000000000000000000000000000000”
N=0
X = “11111111111111111111111111111111”
N=32
X = “10101010101010101010101010101010”
N=16
X = “1110111110111111100111111110001”
int32_t bit_count(int32_t x)
{
int y = 0;
for (int i=0; i<32; i++)
if ((x & (1 << i)) != 0) y++;
return y;
}
Correct implementation in C:
Natural, easy to understand, but inefficient and slow (need 32 iterations)
Easy to simulate, may not be easy to formally verify
N=25

## Slide 60: Synthesis example
int32_t bit_count(int32_t x)
{ x = (x & 0x55555555) + ((x >> 1) & 0x55555555);
x = (x & 0x33333333) + ((x >> 2) & 0x33333333);
x = (x & 0x0F0F0F0F) + ((x >> 4) & 0x0F0F0F0F);
x = (x & 0x00FF00FF) + ((x >> 8) & 0x00FF00FF);
x = (x & 0x0000FFFF) + ((x >> 16) & 0x0000FFFF);
return x;}
Count the number of 1’s in an integer (1)
uint32_t largest_power(uint32_t x){
uint32_t num = 0xffffffff;
while(num!=0){
if(num<x) break;
num = num>>1;
}
return num;
}
uint32_t largest_power(uint32_t x){
uint32_t num = /*** const0 ***/;
while(num!=0){
if(num<x) break;
num = /*** 1 block(>>,|)(num,const1) ***/;
}
return num;
}
(a) Original C codes
(b) Template 1
uint32_t largest_power(uint32_t x){
uint32_t num = 0x7fffffff;
while(num!=0){
if(num<x) break;
num = num>>1;
}
return num;
}
(c) Refined template 1
Given RTL/gate is simulated

## Slide 61: Count the number of 1’s in an integer (2)
uint32_t largest_power(uint32_t x){
uint32_t num = 0xffffffff;
while(num!=0){
if(num<x) break;
num = num>>1;
}
return num;
}
(a) Original C codes
uint32_t largest_power(uint32_t x){
uint32_t num = /*** const0 ***/;
while(num!=0){
if(num<x) break;
num = /*** 1 block(&,|)(num,const1) ***/;
}
return num;
}
(b) Template 2
uint32_t largest_power(uint32_t x){
uint32_t num = 31;
while(num!=0){
if(num<x) break;
num = (uint32_t)1366292263 & num;
}
return num;
}
(c) Refined template 2
int32_t bit_count(int32_t x)
{ x = (x & 0x55555555) + ((x >> 1) & 0x55555555);
x = (x & 0x33333333) + ((x >> 2) & 0x33333333);
x = (x & 0x0F0F0F0F) + ((x >> 4) & 0x0F0F0F0F);
x = (x & 0x00FF00FF) + ((x >> 8) & 0x00FF00FF);
x = (x & 0x0000FFFF) + ((x >> 16) & 0x0000FFFF);
return x;}
Given RTL/gate is simulated

## Slide 62: Count the number of 1’s in an integer (3)
uint32_t largest_power(uint32_t x){
uint32_t num = 0xffffffff;
while(num!=0){
if(num<x) break;
num = num>>1;
}
return num;
}
(a) Original C codes
uint32_t bit_count(uint32_t x){
uint32_t num;
uint32_t mask=1;
for(num=0; mask!=0;mask=/*1 block(&,|,^,>>)(mask,const)*/){
if(/*1 block(&,|,^,>>)(x,mask,const)*/){
num=++;
}
}
return num;
}
(b) Template 4
(c) Refined template 4
UNSAT and no solution found
int32_t bit_count(int32_t x)
{ x = (x & 0x55555555) + ((x >> 1) & 0x55555555);
x = (x & 0x33333333) + ((x >> 2) & 0x33333333);
x = (x & 0x0F0F0F0F) + ((x >> 4) & 0x0F0F0F0F);
x = (x & 0x00FF00FF) + ((x >> 8) & 0x00FF00FF);
x = (x & 0x0000FFFF) + ((x >> 16) & 0x0000FFFF);
return x;}
Given RTL/gate is simulated

## Slide 63: Proposed method
(a) Equivalence checking may be hard
(d) Formal equivalence checking may be much easier
  Generated with templates
Note: Considered as generalized mutation testing
  Template is a general form of set of mutants
(2) RTL/netlist
(1) System level: C
(3) System level: C Template
= Partially missing
(a) Equivalence checking
(3) System level: C Template
= Partially missing
(c) Reconstruction of missing portions by solving QBF problems
(b) Template generation by making small numbers of sentences vacant
(4) System level: C Recovered template
(4) System level: C Recovered template
(d) Formal equivalence checking
(5) Complete test patterns
(5) Complete test patterns
…
…

## Slide 64: Template and its refinement based approach
Template
  Close to complete program codes
  A small number of portions are missing
    Represented as selections of variables, operators, and others. Notation: /*** 1 block(>>,|)(num,const1) ***/;
Closely related to mutation testing
  A mutant is an instance of transformed statement
    E.g., num>>1, num>>2, num>>3, …
    All are covered by the above template
Template based approach should cover more mutants with less numbers of test patterns
  A set of test patterns generated from a template guarantees to cover all instances which can be driven from the template

## Slide 65: Extension for ECO
After generating RTL/gate, ECO is applied only to implementation designs
Try to get a corresponding C from ECOed implementation
Same method can be used
  Implementation designs are only simulated
Experiments are on going
  Here small examples are shown
(2) RTL
(1) Original system design in C
High level synthesis
Or
Manual design
Logic synthesis
Or
Manual design
(3) Netlist
(6) Restored high level design in C
(4) RTL with ECO
(5) Netlist with ECO
Proposed method: Automatic inferring
ECO
ECO
≠
Due to ECO

## Slide 66: Ex: Counting numbers of 1’s in integer
int32_t bit_count(int32_t x)
{
int y = 0;
for (int i=0; i<32; i++)
if ((x & (1 << i)) != 0) y++;
return y;
}
Specification in C (or original design in C)
First ECO does not change the functionality
  It reduces circuit sizes

## Slide 67: Original implementation
xo
int32_t bit_count(int32_t x) {
x = (x & 0x55555555) + ((x >> 1) & 0x55555555);
x = (x & 0x33333333) + ((x >> 2) & 0x33333333);
x = (x & 0x0F0F0F0F) + ((x >> 4) & 0x0F0F0F0F);
x = (x & 0x00FF00FF) + ((x >> 8) & 0x00FF00FF);
x = (x & 0x0000FFFF) + ((x >> 16) & 0x0000FFFF);
return x; }
&
0x55555555
+
&
>>1
0x55555555
&
0x33333333
+
&
>>2
0x33333333
&
0x0F0F0F0F
+
&
>>4
0x0F0F0F0F
&
0x00FF00FF
+
&
>>8
0x00FF00FF
&
0x0000FFFF
+
&
>>16
0x0000FFFF
xi
Note: All bit widths are 32 bits

## Slide 68: ECO(1): More compact implementation
0x55555555
-
&
0x33333333
+
0x33333333
+
&
0x0F0F0F0F
+
>>8
Xin
Note: All bit widths are 32 bits
>>1
&
>>2
&
>>4
+
>>8
Xout
People has found that this also does the same
Formal equivalence checking between the C with for-loop and this with templates (same one for ECO(2))

## Slide 69: Corresponding template and its refined results for ECO (1)
Implementation is simplified significantly
P1: Symbolic constant
P2: Expression of x, mask, and constant
with operators, &, |, and >>
P3: Expression if num and constant
with +, -, &, and |
uint32_t bit_count(uint32_t x){
uint32_t num=0;
uint32_t mask=1, i;
for(i=0; i<32 ; i++){
if( x&mask ) num++;
mask=mask<<1;
}
num= ;
return num;
}
P1
P2
P3
Refined to be the same as the original C
...
for(i=0; i<32 ; i++){
if( x&mask ) num++;
mask=mask<<1;
}
num= num ;
...

## Slide 70: ECO (2): Counting 0’s instead of 1’s
Note: All bit widths are 32 bits
Inverters are added to the input part
0x55555555
-
&
0x33333333
+
0x33333333
+
&
0x0F0F0F0F
+
>>8
Xin
>>1
&
>>2
&
>>4
+
>>8
Xout

## Slide 71: Corresponding template and its refined results for ECO (2)
Inverters are added to the input part
P1: Symbolic constant
P2: Expression of x, mask, and constant
with operators, &, |, and >>
P3: Expression if num and constant
with +, -, &, and |
uint32_t bit_count(uint32_t x){
uint32_t num=0;
uint32_t mask=1, i;
for(i=0; i<32 ; i++){
if( x&mask ) num++;
mask=mask<<1;
}
num= ;
return num;
}
P1
P2
P3
P1=”32”, P2=”!x&mask”, and P3=”num”.
P1=”32”, P2=”x&mask”, and P3=”(32-num)&63”.
Alternative solution was also found:
6 iteration, 2.2 seconds

## Slide 72: ECO (3): Counting 1’s only in the first 16 bits
Note: All bit widths are 32 bits
Last part of the circuit is deleted
0x55555555
-
&
0x33333333
+
0x33333333
+
&
0x0F0F0F0F
+
>>8
Xin
>>1
&
>>2
&
>>4
+
>>8
Xout

## Slide 73: Corresponding template and its refined results for ECO (3)
Inverters are added to the input part
P1: Symbolic constant
P2: Expression of x, mask, and constant
with operators, &, |, and >>
P3: Expression if num and constant
with +, -, &, and |
uint32_t bit_count(uint32_t x){
uint32_t num=0;
uint32_t mask=1, i;
for(i=0; i<32 ; i++){
if( x&mask ) num++;
mask=mask<<1;
}
num= ;
return num;
}
P1
P2
P3
P1=”16”, P2=”x&mask”, and P3=”num”
4 iteration, 0.6 seconds

## Slide 74: ECO (4): Counting 1’s in first 16 bits and counting 0’s in last 16 bits
Note: All bit widths are 32 bits
Input part of circuit is modified
0x55555555
-
&
0x33333333
+
0x33333333
+
&
0x0F0F0F0F
+
>>8
Xin
>>1
&
>>2
&
>>4
+
>>8
Xout
[0-15]
[16-31]

## Slide 75: Corresponding template and its refined results for ECO (4)
Inverters are added to the input part
P1: Symbolic constant
P2: Expression of x, mask, and constant
with operators, &, |, and >>
P3: Expression if num and constant
with +, -, &, and |
uint32_t bit_count(uint32_t x){
uint32_t num=0;
uint32_t mask=1, i;
for(i=0; i<32 ; i++){
if( x&mask ) num++;
mask=mask<<1;
}
num= ;
return num;
}
P1
P2
P3
Unfortunately no solution

## Slide 76: Need another template for ECO (4)
P11=”16”, P21=”x&mask”, P12=”16”, P22=”!x&mask”,
and P3=”num”.
P11, P12: Symbolic constant
P21, P22: Expression of x, mask, and constant
with operators, &, |, and >>
P3: Expression if num and constant
with +, -, &, and |
uint32_t bit_count(uint32_t x){
uint32_t num=0;
uint32_t mask=1, i;
for(i=0; i<32 ; i++){
if( x&mask ) num++;
mask=mask<<1;
}
for(i=0; i<32 ; i++){
if( x&mask ) num++;
mask=mask<<1;
}
num= ;
return num;
}
P11
P21
P3
P12
P22
4 iteration, 1.3 seconds

## Slide 77: Issues
We do not know the complete specification
If a template is correct, i.e., there is a solution inside the template, that solution is guaranteed to be obtained
But if a template is incorrect, i.e., there is no solution inside the template, different situations happen:
  Proposed method says there is no solution: This is good
  Proposed method says there is a solution which is simply wrong: Big problem ***
Right now the only way to go is to use multiple different templates in order to avoid *** cases
  There is a simple example of ***
  However in the experiments never happened