## Slide 1: Debugging integer arithmetic circuits –tutorial
Vikas K Rao (University of UTAH)

## Slide 2: 10,000 feet approach
Verification problem is formulated as mathematical manipulation of specification polynomial over circuit polynomials.
Decimal representation of circuit’s primary inputs and outputs.
Assumes availability of golden specification.
Remainder pattern analyzed and partitioned to fix the buggy circuit.
Gate misplacement and signal inversion that change the functionality of design is the fault model.

## Slide 3: Bug classification and debug flow chart
Single Independent bug
Multiple independent bugs
Single dependent bug
Mixed bug circuits

## Slide 4: Implementation
Remainder generation(backup slides).
Directed test generation
  Figuring out which assignments to primary input variables makes the remainder outputs non-zero.
  SMT solvers used to find assignments.
Bug localization(single faults)
  Simulate tests and compare outputs with golden outputs.
  Backtrack and build gate cones for faulty outputs.
  Prune search space by intersecting multiple faulty output cones(also works for multiple independent bugs).

## Slide 5: Pattern table
Z2 cone – {2,3,4,6,7}
Z3 cone – {2,3,4,6,8}
Independent bugs – search space is intersection –{2,3,4,6}
If it was a dependent bug scenario, then search space –{2,3,4,6,7,8}

## Slide 6: Implementation – multiple independent bugs
Error detection and correction
  Match suspicious gate patterns with remainder pattern starting from level 1 (primary input side).
  If the pattern doesn’t match, store the output of marked gate and add it to dictionary.

## Slide 7: example
Finding faulty primary outputs – simulate and compare
Remainder partitioning
  Construct pattern R = R1 + R2
‘n’ independent bugs mapped to debugging ‘n’ faulty designs.
Question – what if gate 2 is wrong – what about discrepancy in remainder term variables?

## Slide 8: Implementation - Multiple dependent bugs
Bugs sharing faulty input cones.
Faulty gates – union to prune the search space.
Remainder cannot be easily partitioned.
  Construct two patterns for each faulty gate
  For each pattern, compute R-pi and store the result in a dictionary.
Remainder partition claim – “If some of the variables which exist in the term already exist in terms of sub-remainder R1, it will be added to R1, else create a R2 and add it to R2”

## Slide 9: example
Finding faulty primary outputs – simulate and compare.
Remainder partitioning
  Cannot construct R = R1 + R2 directly.
2 dependent faults
  Find R, then construct R1 as if it’s a standalone gate fault.
  R2` should be constructed as R-R1
  Find fault gate patterns in R-R1 dictionary.
Question – more than 2 dependent bugs – complexity is exponential.

## Slide 10: Example contd..

## Slide 11: Approach summary
steps -
  Use non-zero remainders to generate directed test cases.
  Activate bugs (simulate and compare)
  Localize the bugs and build faulty gate cones (union for dependent, intersection for independent)
  Correction (remainder partitioning and remainder pattern match with ref table)
  One gate at a time or multiple dependent bugs at a time
Remainder partitioning (difficult for dependent bugs due to term cancellations and combinations).
Datastructure to store the sub-remainder terms (hash maps and sorted sets)

## Slide 12: What doesn’t it talk about?
Inverters (signal inversion)
Remainder term discrepancies while partitioning.
What if golden specification is not available?
Limitations mentioned in remainder generation paper.
Dependent algorithm experiments are done using only 2 bugs.
Doesn’t talk about wire faults(assumed to be caught in mapping/synthesis tools?)

## Slide 13: Backup

## Slide 14: Backup - 2 bit signed multiplier function extraction – remainder generation

## Slide 15: Key intelligence
Substitution order
  Dependency – substitute all signals in a logical cone
  Levelization – horizontal logic level constraint for common fan-in variable elimination
Fanouts
  Heuristics for common fanout eliminations
Vanishing polynomials
  Some output bits evaluate to zero. Also helps variable simplification at intermediate cuts.
Complex gates
  AOI,OAI – dissecting to simple gates gives greater choice of flexibility in cuts
Binary Signals
  Vanishing polynomial which removes residual expression in forward re-writing
Efficient Datastructure
  C++ objects for pseudo Boolean representation (term and substitution maps)

## Slide 16: Limitations
Circuit Boundaries
  No clear heuristics to define I/O boundaries
Output encoding
  Bits closer to MSB are difficult to be encoded in bigger circuits
Effects of synthesis on function extraction
  Different mapping libraries infer different re-writing times
  Structure dependent as complex gates and optimizations (USP of latest CAD tools) make it harder for redundant gates to exist (helps multiple cancellations)
  Latest commercial tools always head for most optimized function implementation and hence removes redundancy.

## Slide 17: Bug identification of arithmetic circuits
Forward (PI-PO) rewriting
Backward (PO-PI) rewriting
Computing signature difference at cuts
Bug correction table

## Slide 18: Debug Algorithm

## Slide 19: Reference
Farimah Farahmandi, Prabhat Mishra, “Automated Test Generation for Debugging Multiple Unknown Bugs in Arithmetic Circuits”.
M. J. Ciesielski, C. Yu, W. Brown, D. Liu and A. Rossi, “Verification of gate-level arithmetic circuits by function extraction,” in IEEE/ACM International Conference on Computer Design Automation(DAC), 2015, pp. 1–6.
Cunxi Yu, Walter Brown, Duo Liu, André Rossi, Maciej Ciesielski, “Formal Verification of Arithmetic Circuits by Function Extraction”, in IEEE-TCAD, 2016.